Sight Glass  Sample Specification

All Sight Glass Gauge Valves shall be of

thermoplastic construction (PVC or PP) and have

no metal to media contact. PVC shall conform to

ASTM D1784 cell classification 12454-A and PP

shall conform to ASTM D4101 Cell Classification

PP0210B67272. Valves shall be of compact

design and shall eliminate the need for multiple

valves and fittings. Valves shall incorporate a

double O-ring union end design to allow easy

maintenance of the glass, and a drain plug to

permit sampling of fluid. All valves shall be rated to

a maximum of 70 psi at 70 degrees F, as

manufactured by Asahi/America, Inc.